## Slide 1: Simple Machines 14 - 4

## Slide 2: Lesson Objectives
I can name, describe, and give an example of the six types of simple machines.
I can describe how to determine the ideal mechanical advantage of each type of simple machine.

## Slide 3: 6 Different Types of Machines Homer could choose from:
Wheel & Axle

## Slide 4: Input and Output
Input Force (Effort Side)
Push or pull that you have to do to the machine
Example: Pushing keys on a keyboard
Person moves a shovel
Look for green to show the input in this slide show
Output Force (Result Side)
Push or pull the machine
does on the object
Example: What appears
on a computer screen
Shovel moves the dirt
Look for yellow to show
the output in this
slide show
Machines involve two forces to accomplish work. Main Concept 4:
As a result of the Input force, an Output force occurs
and work gets done on an object!

## Slide 5: The Lever
A bar that is free to pivot, or move about a fixed point called a fulcrum when an input force is applied.
Fulcrum = the pivot point of a lever.
There are three classes of levers based on the positioning of the effort force, resistance force, and fulcrum.

## Slide 6: Lever
Input work (Effort Side)
Output work (Result Side)
Force
Force
Basically, this is a board that is placed on a pivot point called a fulcrum
As you apply a force to one side
the other side applies a force to the
object you want moved!
Here is the distance
needed

## Slide 7: First Class Levers
Fulcrum is located between the input (effort) force and output (resistance) force.
Makes work easier by multiplying the effort force AND changing direction.
They will increase the force or distance depending on location of the fulcrum.
Examples: claw of hammer, rowing oars, seesaw

## Slide 8: Second Class Levers
Output (resistance) force is found between the fulcrum and input (effort) force.
MA always greater than 1
Makes work easier by multiplying the effort force, but NOT changing direction.
Output force is greater than input force which causes the input force to be over a greater distance
Examples: bottle opener, wheelbarrow, nutcracker

## Slide 9: Third Class Levers
Input (Effort) force is located between the output (resistance) force and the fulcrum.
MA always less than 1
Does NOT multiply the effort force, only multiplies the distance.
Helpful because they increase the distance through which the output force is exerted.
Examples: Shovel, Tennis racket

## Slide 10: Levers!!!!!!!!!!!

## Slide 11: Mechanical Advantage Levers
Ideal (IMA) =
input arm = distance from input force to the fulcrum
output arm = distance from output force to the fulcrum
Actual (AMA) =

## Slide 12: M. A. of Levers
Force
Work = Input Force x Input Distance Work = Output Force x Output Distance
Distance
Force
Distance
Don’t forget: Work of Input = Work of Output
In this case, with the fulcrum right in the center, the forces,
distance and total input/output work are exactly the same!
Think: when force and
distance are exactly the
same; is there any M.A?
Think: If the Input and Output are exactly
the same is there any point to using a machine?

## Slide 13: So how can we increase M.A. of a lever?
Force
Force
Distance
Distance
We have to adjust how we set up the machine itself!
In this case we can move the fulcrum and change
the distance of the output and input:
Notice that mathematically, even though the amounts of distance and force
have changed the total work done on both sides remains the same!
Notice what happens to
the force and distance of
each side when we move
Fulcrum closer to the mass
Output: Less distance but more force!
Input: More distance but less force!
Work = Output Force x Output Distance
Work = Input Force x Input Distance

## Slide 14: Inclined Planes
A slanted surface used to raise an object.
Make work easier because there is a smaller input force but must be done over a larger distance.
Examples: ramps, stairs, ladders

## Slide 15: Incline Plane
Input work (Effort Side)
Output work (Result Side)
Homer may have to push the box up,
but it takes less effort than simply lifting it
An incline plane is a ramp that increases the distance needed to
move an object but makes the work easier to do.
Think: has the distance
required changed?
Where is the input and
output sides?
The work has been spread out over a greater distance than lifting straight up!
Therefore it is easier to accomplish (takes less effort)!

## Slide 16: Mechanical Advantage Inclined Planes
Ideal (IMA) =
Actual (AMA) =
MA can never be less than 1.
Ideal (IMA)

## Slide 17: M.A. of an Incline Plane:
To give this simple machine more mechanical advantage, simply make the ramp longer
Notice: Did the height of the ramp change?
The same amount of work was accomplished with less force on your part!
The ramp is now
longer and less steep
Distance
Work that needs to
be accomplished

## Slide 18: Wedges
A double inclined plane that moves or v shaped object whose sides are 2 inclined planes sloped towards each other
Increase MA by sharpening, make wedge longer, make wedge thinner
Examples: knife, axe, razor blade

## Slide 19: Wedge:
Output Force
Input Force
A wedge works like two
ramps put together.
As the input force pushes down, the output force pushes out, splitting the object

## Slide 20: Screws
An inclined plane wrapped around a cylinder.
Examples: bolts, augers, drill bits

## Slide 21: Mechanical Advantage Screws
Ideal (IMA) =
Actual (AMA) =
Increase MA by
Threads on the screw closer
Spiral on the screw longer

## Slide 22: Wheel and Axle
A lever that rotates in a circle.
A machine consisting of a combination of two disks or cylinders (wheels) of different sizes (radius).
Smaller wheel is termed the axle.
Examples – Doorknobs, ferris wheels

## Slide 23: The Wheel & Axle
Either the axel turns the wheel or
the wheel turns the axel.
The input and output of a wheel and axel
will all depend on how you use it.
If it is used as a wheel to move a car (or something like it)
Then the input comes through the axel and the output is from the turning of the wheel
If it is used as steering wheel to turn (or something like it)
Then the Input comes through the wheel and the output is from
the axel
Q: How could Homer use a wheel
and axle to lift his box?

## Slide 24: Homer turns the crank on the wheel and the box on the ramp moves up
Don’t forget!
This is the work Homer
Is trying to do!
= Lift the box this distance
Now you would have to ask when a machine this size
would be worth the effort to make it
Maybe if there were a lot of boxes
to lift = more work to do

## Slide 25: Mechanical Advantage Wheel and Axle
Ideal (IMA) =
Actual (AMA) =

## Slide 26: Pulleys
A chain, belt , or rope wrapped around a wheel.
Can either change the direction or the amount of effort force
Ex. Flag pole, blinds, stage curtain

## Slide 27: Pulley Types
FIXED
Can only change the direction of a force.
Does not increase the force and is attached to something that does not move
MA = 1
MOVABLE
Can multiply an effort force, but cannot change direction
Causes input force over a greater distance.
Attached to the object being moved
MA = 2
Block and Tackle
Fixed pulley and movable pulley used together.
Can have large MA if several pulleys used together.
MA = > 2

## Slide 28: Pulleys
Input Work (Effort Side)
Output (work side)
A pulley is a wheel with a rope wrapped
around it and attached to the object
you want to move.
When you apply a pull force to one side
of the rope, the rope applies a pull
force to the object side
and the object gets lifted
Force
Force
Think: has the distance
required changed?
Which side of the pulley is the
input and which is the output?

## Slide 29: Mechanical Advantage Pulleys
Ideal (IMA) = # of supporting Ropes
Actual (AMA) =

## Slide 30
MA = Count # of ropes that apply an upward force (note the block and tackle!)

## Slide 31: M.A. of Pulleys:
Input Work (Effort Side)
Output work side
When you use a basic single pulley
setup, the M.A. = 1
Force
Notice that the force and
distance is equal
Distance
Distance
Force
In order to get M.A. you need to
change the distance of your input pull!

## Slide 32: Movable Pulleys give M.A.
Output (Resultant Side)
Input (Effort Side)
Work = Force x Distance
Work = Force x Distance
Force
Distance
Distance
Pulleys only have mechanical advantage when you use a moveable pulley with your setup.
Force
When you increase the Input distance, the Input force automatically goes down and the Output force automatically goes up!!!
Notice that you have to pull more rope to
accomplish the same output distance.
This is the point! More Input distance will lessen
then amount of Input force needed!
Watch the difference in distance for
Input and the Output!

## Slide 33
Input Force (Effort)
Output Force (Result)
Pulleys only have mechanical advantage when you use a moveable pulley with your setup.
By making a combination of Pulleys, we are adding
even more input distance, which should lower out
Input force even more = more M.A.!!!
Movable + Fixed Pulley Combination (“Block and Tackle”)
Moveable Pulley
Fixed Pulley

## Slide 34: Compound Machines
A combination of two or more simple machines.
Cannot get more work out of a compound machine than is put in.
Usually have a low MA because the more moving parts the more friction

## Slide 35: Compound Machine
Slow
Fast
The use of a wheel and axle are actually very common
The rear wheel turns more for each time you
pedal causing you to travel farther with less force

## Slide 36: “Compound Machine” Any combination of several simple machines…
A compound machine is simply two or more simple machines put together.
Notice that there are at least 4 different
simple machines in this one compound machine
Simple machines are most often used
in combinations like this!

## Slide 37: Big Ideas
A compound machine is a combination of 2 or more simple machines.